## Slide 1: Bridging the Digital Infrastructure gap in Rural India – “Last Mile-as-Managed Service”
Satyaspeak
ITU – RDF on ICT Infrastructure as a basis for Digital Economy
Kiev, Ukraine
14-16 May, 2019
SATYA N. GUPTA
Secretary General - ITU-APT Foundation of India
Chairman - BLUETOWN, India

## Slide 2
For successful deployment of the Broadband in the rural areas it is necessary for the respective government agencies/public institutions/Telecom Service Providers to provide the existing backhaul infrastructure at a subsidised cost on Revenue Share basis.
For Broadband backbone network, optic fiber is the best and future proof solution with long term perspective. It needs to be funded by Government/USO agency and investment treated as sunk cost for the purpose of societal return on investment like any other national infrastructure such as highways, Railroads, Power and other public utilities.
For the access network, it is advisable and cost effective to go for unlicensed spectrum based (Wi-Fi) Access solution with different Backhaul technologies depending upon the terrain, geography and existing infrastructure, availability of conventional telecom system and backbone network etc. This should generally be funded by the local service providers/third party independent infrastructure provider.
Implementable and Cost-Effective Solution for Rural Broadband Access

## Slide 3
Local Entrepreneur/Infrastructure Provider
Public Funding
Third Party
Local Entrepreneur
Public Funding for Backhaul & Content
Local Community
Layer 1
Layer 2
Layer 3
Layer 4
Customer Services Provision
Access
Infrastructure
Backhaul
Infrastructure
Content & Application
Infrastructure
Full Public Funding of Infrastructure
Community Funding
Local Entrepreneur
Public Funding for Backhaul & Content
Operator Funding
Local Entrepreneur
Funding Options for Rural Broadband Infrastructure
(Based on Analogy from Alberto on Public-Private interplay)

## Slide 4: Funding Options for Rural Broadband Infrastructure
Full Public Funding: The investment and the ownership of the network remains with Government/its agency, the design build and operate is generally outsourced to a non-government entity who has the expertise in implementing such projects.
Public Funding of Backhaul and Content, Community funding of Access Network: Government and USO funding is limited to Backhaul and content infrastructure, which forms the major Capex, whereas the Access network is funded by the local bodies and community from their sources.
Public Private Partnership (PPP)- Backhaul and Content Public Funded, Access Network Private Funded: Backhaul infrastructure is funded by Government/USO/ Public Sector, the Access Network is funded by the service provider/operators themselves. The VLE is employed as the franchisee of the service providers to manage the customer service provision.
Public Private Partnership (PPP)- Backhaul Public Funded, Content and Access Private Funded: This is emerging model in cases where operators have no interest in any investment but there are 3rd party entrepreneurs, who are willing to invest and manage the access network and service provision.
Contd…

## Slide 5
Technology Options Local Conditions | Distributed wireless based Backhaul + Wi-Fi Access working on renewable energy | Distributed wireless based Backhaul +Wi-Fi Access + voice working on renewable energy | Satellite Backhaul + Wi-Fi based Broadband Access working on renewable energy | Wireless Broadband Access through telecom network using TV set as Access device | Wi-Fi based Broadband Access with fiber Backhaul
Rural and Remote areas with no grid supply and no telecom network | Yes Good for low OPEX and CAPEX | Yes Good for low OPEX and CAPEX | Yes Good for high OPEX and low CAPEX | NA | NA
Rural and Remote areas with no reliable grid supply but with mobile network | Yes Good for low OPEX and CAPEX | NA | Yes Good for high OPEX and CAPEX | NA | NA
Rural and Remote areas with no grid supply but with fiber Backhaul | Yes Good for low OPEX and CAPEX | Yes | NA | NA | Yes
Rural and remote area with grid power and mobile network | NA | NA | NA | Yes Ideal for TV owning households | Yes
Suitability Of Technology Options for Rural Broadband Access

## Slide 6
Key Partners PSU Telcos Private Companies ISPs/TSPs Social Networking/ Content companies Investors, VCs NGOs Academic Institutions System Integrators | Key Activities Local Manufacturing & Sourcing Alliances & Partnership formation Proposal & Responses to EOI/ Tenders Sales & Promotions | Value Proposition Low cost, Low power & Low maintenance (3L) High QOS & Coverage Multi-faced system Rugged, Rural, Outdoor fit Open platform (Standard Wi-Fi APs) Environment friendly green-solution DG-less) End-to-End IP platform Cloud server for localized content |  | Customer Relationships 24*7 Customer Care Centre Micro Operators/ VLEs Regional Sales Executives | Customer Segments Rural Retail Market Govt. users in villages Institutional users SOHO (Small Office Home Office)
 | Key Resources Investors & Venture funding Proven Technical Solution Innovative Business Model Passionate Management |  |  | Channels Micro Operators/ VLEs Co-branded outlets Partnership Telcos/ISPs CSC (Common Services Centers) Direct Sales | 
Cost Structure Manufacturing & Sourcing Wi-Fi hotspot integration, funding, deployment, operation & maintenance Employees & office R&D & Training Sales & Marketing |  |  | Revenue Streams Sales of Prepaid Vouchers to retail customers Content/ Application services revenue share Postpaid Connections to institutions/ SOHO Govt. Anchor usage payments receipts Mobile Data offload revenues |  | 
Business Model Canvas- Managed Rural Broadband Service Provider

## Slide 7
For provisioning of Broadband in such rural areas a MHSP in partnership with Telco/ISP, installs a 5-meter-high pole/mast mounted microwave backhaul radio and Wi-Fi hotspot with solar panel and Li-Ion/SMF batteries along with BTS all in a box mounted on this mast.
MHSP will appoint a Village Local Entrepreneur (VLE) from Local folks for managing Hotspot.
This VLE will be given basic training by the MHSP for regular maintenance and operation of Hotspot infrastructure and to provide Wi-Fi of assisted Broadband services to the villagers.
The VLE working as franchisee of MHSP, acts as single point of contact for all Broadband related products and services.
VLE also takes the responsibility of digital literacy and assisted Broadband services (such as e-governance) to the rural masses.
VLE will also use this WI-FI infrastructure for generating revenue through other activities (such as mobile charging providing rail-road ticketing, getting market prices of crops and assisting in doing business transactions, rural e-banking, help in getting medical facilities from urban health centers etc. to name a few).
Business Model for Rural Broadband Access - Managed Hotspot Service Provider

## Slide 8
MHSP funded through Managed Services (CAPEX)/Revenue share (OPEX) route
Investment by VLE through Micro-Financing/ Startup Fund
Subsidy by Government/ Local bodies Contribution/ Direct benefit to users through USO fund, Guaranteed Revenue by the Anchor Users (Govt.)
Funding options for Managed Hotspot Service Provider (MHSP)

## Slide 9
MHSP
To create a sustainable social business in PPP mode.
To make use of existing underutilized infrastructure of Telcos.
To innovate and deploy out of box low cost solutions in a business manner.
To add value to stakeholders as well as society.
VLE
Opportunity to become an Entrepreneur.
Contributing to the village community for improving the quality of life, in addition to generate employment and livelihood for self.
Village People
Assisted Broadband services at doorstep/hands.
24/7 connectivity to the Internet.
Improved productivity, efficiency and life style enhancement.
Key benefits of MHSP Business Model

## Slide 10
Why Wi-Fi? : A Killer Technology for ‘Last Mile Broadband Access’
Ubiquitous – Each smart device (including Mobile Phones) is Wi-Fi enabled.
Uses unlicensed spectrum (ISM Band) which is free (750 MHz in 2.4GHz and 5GHz Band).
All IP Technology which is very efficient and future proof which is based on open and ever evolving standards of IEEE (802.11x).
Plug-n-Play ecosystem.
Low Power consuming and Low Cost – overall infra cost about 10% of licensed mobile infrastructure.
Potential to conserve scarce licensed spectrum through Mobile Data Offload (MDO).
NINENP (Non- Interfering, Non-Exclusive, Non-Protected) – Free for All.
Current Hotspots in India – 3.75 Lakhs (mushrooming everywhere).
Potential to deliver 4G and 5G type services through upgradation (802.11ac - Wave2, 802.11ax – Wi-Fi 6)
Ideal futuristic platform for IoT, M2M and E-health, E-farming, E-education.

## Slide 11
100M+ subscribers across the world in next 5 years, 10,000 Managed Hotspots in Rural India
Aspiration
Offering
Technology
Customers
Access Infrastructure built using the License – Free Band available (2.4Ghz, 5 Ghz)
Managed Hotspots at village level using innovative 5L technology (Low Cost, Low Power, Low Maintenance, Local Control, Local Content)
To enable Broadband access to Rural India
BLUETOWN Rural Wi-Fi Initiative
Telcos, ISPs, Local Govt. Bodies, through long term revenue share partnerships

## Slide 12: Bridging the Last Mile gap in PPP Mode – BLUETOWN as MHSP
BSNL, a govt. Telco in India have created 782 GSM (2G) sites in the un-connected areas of the state of Jharkhand.
The State Government in line with the Digital India Mission decided to convert these 782 GSM sites into Wi-Fi hotspots for internet connectivity.
State Government provided support in the form of “Viability Gap Funding” to support BSNL to convert these sites into Wi-Fi hotspots as a anchor beneficiary.
BLUETOWN, a Danish technology startup partnered BSNL to execute, operate, manage and market the project as MHSP.

## Slide 13: Scope of the Project
Existing 2G sites converted to Wi-Fi hotspot by BLUETOWN
2 Mbps of Internet Leased Line provided at each site by BSNL
4 Access Points installed at each site
Customized billing plan (as per the recommendation from state Government) for the end users offered
Centralized Billing platform established
24x7 centralized Monitoring of the sites ongoing
SLA Compliance as per the Govt. requirement

## Slide 14: Wi-Fi Solution Deployed
BLUETOWN Outdoor Solution – Everything on Tower
  Access Point Controller (Housed in an IP67 weahter proof outdoor box)
  3 sector Antenna assembly located on BSNL existing Tower. This includes the following components
    120 Degree Sector Antennae’s (3 in Number)
    Bandpass filters (3 in Number)
    2.4 Ghz Access Points (3 in Number)
    Backplates to support the Antennae assembly (3 in Number)
    Antennae Mounts
  Solar Power system including the following
    Solar Power Unit with Li-ion Batteries (Housed in an outdoor IP67 box)
    Solar Panel
    Solar Cables & Connectors
  4th Access Point with an OMNI/Sector Antennae (as per requirement) to be installed at a location upto 1 Kms (like a school, PHC or GP etc.) away from the tower
  Internet backhaul provided by BSNL

## Slide 15
Unlicensed Microwave Backhaul
EVERYTHING ON TOWER (EOT) - Innovative & Techno-feasible Connectivity Solution for Rural Broadband Access
Omni/directional Antennae
Access Point
Access Point Controller + AAA + Power Unit + Battery + Content Server (LOCAL CLOUD)
Filter
Solar Panel
From Telcos/NBN/Fiber Node/Satellite
Unwired Rural Tower/Mast/Pole/Structure (5-15m)

## Slide 16: BLUETOWN Wi-Fi Solution Salient Features
120 degrees sector antennae used to provide a 360 degree coverage
Solution can be customized in terms of placement of the sectoral antennae and the additional access point
Users connects to the BLUETOWN base station via Wi-Fi within up to 1 Kms in range (diameter)
Users connects via traditional Wi-Fi enabled devices (handsets/tablets/laptops)
Integrated SMF/Li-Ion battery based solar powered solution (35-40 Hours of Backup); more than 5 Years of Battery life
BLUETOWN Wi-Fi AP Controller which is core of the solution is capable of handling:
    AAA Authentication
    Bandwidth Management & RF Control
    Power Control & Battery Management
    Remote Access for system maintenance

## Slide 17
1. For Government & Public Agencies:
Organise “Funding and Build” of National Broadband Network (NBN) to take the Broadband connectivity to rural and remote areas through infrastructure budget/USO funding.
Provide the Backhaul connectivity to the Access Service Providers/VNOs/MHSPs in rural areas on Open Access basis at nominal Incremental charges, through revenue share.
Provide tax breaks/concessions incentives, subsidies for the MHSP as well as Service Providers in rural areas.
Establish the ‘Content Delivery Network’ as a backend/ Cloud platform for the delivery of government services and applications to citizens.
Provide Affordability-Deficit-Funding (ADF) as guaranteed revenue or financial incentive (benefit) for the procurement of Broadband access to public institutions and individuals in rural areas.
Create a light-regulated class license (like the one recommended by regulator – PDOA/PDO) through registration process as is done for OSPs/VAS players.
Recommendations from India Case Study for MHSP

## Slide 18
2. For Local Government Bodies:
Provide free/low cost Access to real estate as well as “Right of Way” for creation of Broadband access network (Hotspots).
Provide exemption/reduce levies for the local taxes including GST for the Broadband equipments and services in rural areas.
Provide initial funding/grant to Village Local Entrepreneurs(VLE) to start Broadband services business and create awareness about Broadband services and applications among the masses.
3. For Regulatory Bodies:
Facilitate ‘Open Access’, ‘Wholesale Pricing’ and ‘Infrastructure Sharing’ for the government/public sector owned facilities to enable the local Internet Service Providers/ VNO’s to provide Broadband services fast and within affordable level.
Permit franchising arrangements between the ‘Operator’ and the Local Entrepreneur (VLE) and to create a light-handed, “Class” license/rural VNO category for niche rural areas by automatic registration process like OSP (Other Service Providers) without any conditions or obligations.
Have ‘Technology-neutral’ and ‘Service-agnostic’ approach to enable the Players to innovate on the technology front to reduce costs.
Make more spectrum ‘license-exempt’ for use of Wi-Fi for Broadband access as well as ‘Middle Mile’ in rural areas as done in India.
Contd…
Recommendations from India Case Study for MHSP

## Slide 19
4. For Operators & Service Providers:
Partner with Managed Hotspot Service Provider (MHSP) to build access network in rural areas using innovative low cost solutions to run on revenue share basis.
Provide interconnectivity to the “Class” licensed local access providers/VNO’s in rural areas on revenue share basis.
5. For MHSPs/Local Communities/NGOs:
Bring awareness and provide training to the local masses to become digital-literate.
Appoint and train the local entrepreneurs (VLE) to take up and manage the Broadband service provisioning.
Facilitate initial funding for the business requirements of Local entrepreneurs (VLE).
Help in identifying the Local Content and Applications requirements.
Contd…
Recommendations from India Case Study for MHSP

## Slide 20
Thank You
Satya N. Gupta
sg@bluetown.com